## Slide 1
HACK THE HORIZON 2.0 · KPR Institute of Engineering and Technology
IEEE Computational Intelligence Society
HTH-SA-06 | SMART CITY / MUNICIPAL ENERGY
SMART ADAPTIVE
STREET LIGHTING
Occupancy & Footfall-Responsive Intelligent Lighting System
“Light only when needed. Respond instantly when it matters.”
An IoT-enabled adaptive lighting system combining ambient-light sensing, motion detection, intelligent brightness control, energy monitoring and distributed ESP32 communication.
LDR + PIR
ESP32
Adaptive LED
Energy Monitoring
TEAM NAME | Saveetha School of Engineering, SIMATS | TEAM MEMBERS
PIR: MOTION → 100%
IDLE · ~25%
Concept illustration

## Slide 2
02 · THE PROBLEM
Street Lights Stay ON Even When the Street Is Empty
HACK THE HORIZON 2.0 | HTH-SA-06 | SMART ADAPTIVE STREET LIGHTING
2 / 10
Conventional street lighting is typically controlled using fixed schedules or continuous illumination. During low-traffic periods, this can cause unnecessary energy consumption, while safety still requires rapid illumination when pedestrians or vehicles approach.
LOW TRAFFIC
Large portions of the night can have very low pedestrian and vehicle activity.
ENERGY WASTE
Full-brightness lighting during idle periods consumes energy unnecessarily.
SUDDEN MOVEMENT
A pedestrian or vehicle can enter the lighting zone unexpectedly.
SAFETY REQUIREMENT
Lighting must respond rapidly enough to provide full illumination.
CONVENTIONAL
Fixed Schedule
Fixed Brightness
Unnecessary Energy Use
INTELLIGENT
Ambient + Motion Detection
Adaptive Brightness
Energy Saving + Safety
How can we reduce energy consumption without compromising safety?
The goal is not to turn street lights OFF — it is to make them SMART.

## Slide 3
03 · OUR SOLUTION
A Distributed 3-ESP32 Intelligent Street-Lighting System
HACK THE HORIZON 2.0 | HTH-SA-06 | SMART ADAPTIVE STREET LIGHTING
3 / 10
Our system continuously senses the environment, detects movement, adapts lamp brightness, monitors energy usage and reports real-time status through a central monitoring node.
ENERGY NODE
Mini ESP32 #1
Piezo micro-energy harvesting
Battery monitoring
Voltage + current sensing
Power management
Wireless energy-status reporting
LIGHTING NODE
Mini ESP32 #2
LDR ambient-light sensing
PIR motion detection
Adaptive LED brightness
Safety response measurement
Wireless lighting-status reporting
CONTROL NODE
Main ESP32
TFT monitoring
Buttons / manual override
Buzzer alerts
Central data collection
System status
ONE Wi-Fi NETWORK
SENSE
DECIDE
RESPOND
MEASURE
OPTIMIZE

## Slide 4
04 · SYSTEM ARCHITECTURE
Three Specialised Nodes. One Network. One Control Centre.
HACK THE HORIZON 2.0 | HTH-SA-06 | SMART ADAPTIVE STREET LIGHTING
4 / 10
ONE Wi-Fi NETWORK
MINI ESP32 #1
ENERGY NODE
Piezo Disk
Capacitor
Charging Module
Li-ion Battery
Current Sensor
Voltage Sensor
DC-DC Power
MINI ESP32 #2
LIGHTING NODE
PIR Sensor
LDR Sensor
LED Street Light
MAIN ESP32
CONTROL CENTER
TFT Display
Buttons
Buzzer
SENSING
PROCESSING
COMMUNICATION
LIGHTING
ENERGY MONITORING
USER INTERFACE
Energy Node → Wi-Fi → Main ESP32 · Lighting Node → Wi-Fi → Main ESP32 · Main ESP32 → Monitoring / Control / Alerts
Each node performs a specialised function while the central controller provides unified monitoring and control.

## Slide 5
05 · HOW THE INTELLIGENT LIGHTING WORKS
Adaptive Brightness Based on Ambient Light + Movement
HACK THE HORIZON 2.0 | HTH-SA-06 | SMART ADAPTIVE STREET LIGHTING
5 / 10
DAY
OFF
High ambient light
NIGHT + NO MOTION
20–30%
Low-power standby
NIGHT + MOTION
→ 100%
Rapid ramp-up
POST-MOTION
→ 20–30%
Controlled dimming
DECISION LOGIC
1
Read LDR
Ambient light sufficient?
2
Daytime
Lamp OFF / minimal
3
Night
Low standby brightness
4
Read PIR
No → stay low
Yes → ramp to full
5
Timeout
No motion → gradual return to standby
CORE CONTROL LOOP
LDR
PIR
ESP32 Decision
PWM
LED
20–30% are example control values, tunable during testing — not measured results.

## Slide 6
06 · ENERGY HARVESTING & POWER MANAGEMENT
Monitoring Every Watt Through the Energy Node
HACK THE HORIZON 2.0 | HTH-SA-06 | SMART ADAPTIVE STREET LIGHTING
6 / 10
Piezo Disk
Supplementary micro-energy harvesting
Rectify / Condition
Electrical pulses → usable DC
Capacitor
Filtering / energy stabilization
Charging Module
Battery charging management
Li-ion Battery
Energy storage
Fuse
Electrical protection
DC-DC Rails
Boost / buck: 3.3 V · 5 V · 12 V
MEASURE → CALCULATE
Voltage Sensor → V
Current Sensor → I
P = V × I
E = P × t
MEASUREMENT CARD
Measured during final test
Voltage
X.XX V
Current
X.XX A
Power (V × I)
X.XX W
Battery
XX %
Harvested energy
X.XX mWh
The piezo subsystem is a supplementary energy source for the prototype. Its harvested contribution is measured and reported rather than assumed to power the complete street-light load. The current sensor measures current; power is calculated.

## Slide 7
07 · SAFETY + ENERGY SAVINGS
Two Things We Must Prove
HACK THE HORIZON 2.0 | HTH-SA-06 | SMART ADAPTIVE STREET LIGHTING
7 / 10
A · SAFETY RESPONSE
Motion Detected
ESP32 Processing
Brightness Command
LED Ramp-Up
100% Brightness
T_response = T_full_brightness − T_motion_detected
Measured response
XX ms
Defined safety bound
XX ms
Result
PASS / FAIL
Placeholders — measured during final test
B · ENERGY SAVINGS
BASELINE: Always-ON / fixed brightness
ADAPTIVE: low idle + full on motion
Chart: 
| 0h | 1h | 2h | 3h | 4h | 5h | 6h | 7h | 8h | 9h | 10h | 11h | 12h
Baseline | 0 | 8.3 | 16.7 | 25 | 33.3 | 41.7 | 50 | 58.3 | 66.7 | 75 | 83.3 | 91.7 | 100
Adaptive | 0 | 2.7 | 5.4 | 8.1 | 10.8 | 13.5 | 16.3 | 19 | 21.7 | 24.4 | 27.1 | 29.8 | 32.5
Illustrative shape (25% idle, 10% active) — not measured
Saving % = [(E_baseline − E_adaptive) / E_baseline] × 100
Safety response is verified by measured latency, while energy efficiency is verified against a baseline.

## Slide 8
08 · 24-HOUR SMART STREET SIMULATION
Lighting Behavior Changes With Time, Environment and Activity
HACK THE HORIZON 2.0 | HTH-SA-06 | SMART ADAPTIVE STREET LIGHTING
8 / 10
NIGHT
EARLY AM
DAYTIME · OFF / MINIMAL
EVENING
LATE NIGHT
BRIGHTNESS % vs TIME
Chart: 
| 12 AM |  |  |  | 4 AM |  |  |  | 8 AM |  |  |  | 12 PM |  |  |  | 4 PM |  |  |  | 8 PM |  |  |
Low traffic | 25 | 25 | 25 | 25 | 25 | 26 | 26 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 28 | 28 | 26 | 26 | 26 | 26
High traffic | 28 | 28 | 28 | 29 | 29 | 30 | 30 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 48 | 48 | 44 | 42 | 40 | 38
MOTION EVENTS / HOUR (activity)
Chart: 
| 12 AM |  |  |  | 4 AM |  |  |  | 8 AM |  |  |  | 12 PM |  |  |  | 4 PM |  |  |  | 8 PM |  |  |
Low traffic | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 7 | 8 | 6 | 7 | 8 | 6 | 7 | 8 | 6 | 7 | 8 | 8 | 8 | 2 | 2 | 2 | 2
High traffic | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 37 | 28 | 31 | 34 | 37 | 28 | 31 | 34 | 37 | 28 | 55 | 55 | 55 | 45 | 40 | 35 | 30
LOW-TRAFFIC SCENARIO
Few motion events
Longer low-brightness periods
Higher potential energy savings
HIGH-TRAFFIC SCENARIO
Frequent motion events
More full-brightness periods
Increased energy demand
SIMULATED traffic / sensor data for the MVP — not field-measured (example timeout: 20 s per event)

## Slide 9
09 · LIVE MONITORING & PROTOTYPE
One Dashboard. Complete Street Status.
HACK THE HORIZON 2.0 | HTH-SA-06 | SMART ADAPTIVE STREET LIGHTING
9 / 10
PROTOTYPE CONCEPT
ENERGY NODE
ONLINE
LIGHTING NODE
ONLINE
MAIN NODE
ONLINE
Wi-Fi
Illustration — not a photograph of the actual hardware
SMART STREET LIGHT
AMBIENT
XX %
MOTION
DETECTED
LIGHT
100 %
RAMP
XX ms
SAFETY
PASS
VOLTAGE
X.XX V
CURRENT
X.XX A
POWER
X.XX W
BATTERY
XX %
SAVING
XX.X %
Mockup — placeholder values
ENERGY NODE · ONLINE
LIGHTING NODE · ONLINE
MAIN NODE · ONLINE
● Wi-Fi connected
Button 1 → Auto / Manual
Button 2 → Brightness Override
Button 3 → Screen / Node Select
Buzzer → Alerts / Faults

## Slide 10
10 · IMPACT, SCALABILITY & CONCLUSION
From a Smart Prototype to a Smarter Street
HACK THE HORIZON 2.0 | HTH-SA-06 | SMART ADAPTIVE STREET LIGHTING
10 / 10
ENERGY EFFICIENCY
Reduce unnecessary full-brightness operation during idle periods.
SAFETY
Rapidly increase illumination when movement is detected.
VISIBILITY & MONITORING
Real-time lighting, energy and system-health information.
SCALABILITY
Extend from a prototype street segment to a network of connected city lighting nodes.
FUTURE EXTENSIONS
Traffic-density-aware lighting
Weather / fog / rain adaptation
Fault detection
Predictive maintenance
Solar integration
Remote municipal dashboard
AI-based traffic prediction
Sense
Decide
Respond
Measure
Optimize
The future of street lighting is not simply brighter lighting — it is smarter, responsive and measurable lighting.
HTH-SA-06 | SMART ADAPTIVE STREET LIGHTING TEAM NAME | Saveetha School of Engineering, SIMATS